## Slide 1
OpenC2 & Network Telemetry:
Feeding needed data to OpenC2 Applications
Eric Voit
Principal Engineer
evoit@cisco.com
19-May-2017

## Slide 2: Agenda
Telemetry OpenC2 Relationship
Asynchronous Network Subscriptions
OpenC2 relevant Use Cases

## Slide 3: Telemetry OpenC2 Relationship

## Slide 4
Streaming Telemetry
Subscriptions
Let’s push a whole lot of data to where it is useful
Notes: https://commons.wikimedia.org/wiki/File:BigData_2267x1146_white.png#/media/File:BigData_2267x1146_trasparent.png

## Slide 5: Network Policy Feedback Loop
Authoritative Network Data
Authoritative Decisions
Applications
Current Configuration &
Operational State
Flow fingerprints
Interface up/down
Instantaneous config
Instantaneous topology

## Slide 6: Telemetry – Feeding Data to OpenC2 Applications
Authoritative Network Data
Authoritative Decisions
Complete representation
Admission Control
Per-object security
Custom contents
Non-repudiation
Self describing
Subscribable
Low latency
Standard
High volume
Prioritized push
Burst Dampening
Transport options
Multiple recipients
Structured & filterable
Synchronized intervals
Current Configuration &
Operational State
Requirements
Applications

## Slide 7: Data Transfer Mechanisms
Authoritative Network Data
Authoritative Decisions
 | CLI | SNMP | Traps | Syslog |  | YANG
Asynchronous |  |  |  |  |  | 
Scale |  |  |  |  |  | 
Standard |  |  |  |  |  | 
Structured |  |  |  |  |  | 
Complete |  |  |  |  |  | 
Security |  |  |  |  |  | 
Stable |  |  |  |  |  | 
Current Configuration &
Operational State
Legacy (insufficient)
Emerging (objective is to get all to green)
Applications

## Slide 8: Asynchronous Network Subscriptions

## Slide 9: The “Push Zone”
Required Notification Latency
Event Frequency
1 second
1 minute
1 day
1 month
1 hour
0.1 second
1 second
1 minute
1 day
1 hour
0.1 second
Northbound
Pull Protocols
Routing &
Switching
Protocols
BGP
OSPF
CLI
SNMP
Traps
SONET
ARP
Ethernet
Crypto
Keys
Software
Version
Configuration
Data
ACL
Flow
Records
Event
Traps
Counters
Syslog
Operational
Data
Legend
ASIC stats
Topology
Synchronous
Asynchronous

## Slide 10: Asynchronous Push has become a “MUST”
Subscribing
Subscribing
Continuous Polling
Datastore
Continuous Polling
Datastore
Anything different?
No.
NO!
Yeah.
Just the new stuff
fetch
push
  Up-to-date objects delivered
    Reaction speed
    CPU, Bandwidth reduced
  Well known cost/scale limits with continuous polling
    Propagation latency
    CPU, Bandwidth
    Multiple Polling devices

## Slide 11: YANG Subscriptions Concept
Datastore
Streaming of updates
  Customized to recipient
  Encoding (XML, JSON, …)
  Transport (NETCONF, HTTP/2, …)
Publisher
Streaming
mechanism
Subscription
interface
Subscribing to updates
  Any YANG object / subtree on device
YANG

## Slide 12: Two Types of Subscriptions
    On Change
    Push on Object change
Datastore
Publisher of Object Deltas
Subscriber
    Periodic
    Push Object every ‘X’ seconds
Datastore
Publisher of Objects
Subscriber
regular cadence
asynchronous notification
uses ‘Patch’ syntax (add, change, delete)
sends a complete object set every time

## Slide 13: Result → Network Element Feedback Loop
Controller
OpenC2 Application
Application
  Controllers holding network state can publish operational and config info
  Also viable as part of fast reacting multi-layered abstraction
Network
Element
Subscriber
Publisher
Subscriber
Publisher
CLI
YANG

## Slide 14: OpenC2 relevant Use Cases

## Slide 15: Subscribable Objects
Controller
Troubleshooting
Network Element
Network
Element
Capacity Management
Oper Status
Config
Oper Status
Counters
Routes
Config
Routes
Oper Status
Config
Security
Counters
Oper Status
Routes
Config
Flows
Datastore
Counters
Oper Status
Routes
Config
Flows
Notes:   (Use PPT View for animations)

## Slide 16: OpenC2 Use Case & Subscribable Objects
Use Case | Cares about | Subscribe to? |  |  |  | 
 |  | Config | Oper Status | Routes | Counters | Flows
Block on Indicators | Potential Indicators of compromise |  |  |  |  | 
Host Remediation | Current running processes & config |  |  |  |  | 
HBSS Signature | Environmental conditions |  |  |  |  | 
Mitigate Evil Domain | Control & Data Plane activity |  |  |  |  | 

## Slide 17: Host Remediation & Block on Indicators with On-change Push
running software version
IP addresses of neighbors
logged on users
ACL configuration
physical hardware
software checksums
keys in keychain
Cisco’s Intrusion Detection Application currently polls for changes ~2x a day
With on-change, the intrusion detection goes from hours to sub-second
Intrusion Detection Application
Controller
Subscription
OpenC2

## Slide 18: Mitigate Evil Domain with Periodic or On-change Push
Data Center Enclave
Inbound traffic monitored for indicators
On anomaly, immediately bridge in assets such as DDoS scrubbers and IDS for origin subnet(s)
OpenC2
DDoS
Scrubber
VM
Traffic counters
Inter-packet-gap histogram
QoS queue drops
Server response time
Late responses
Attacker
Anomaly
Detection
Subscription
Botnet
IDS

## Slide 19: Telemetry / Subscription: IETF & Google Code Available for Each Path
draft-ietf-netconf-subscribed-notifications
draft-ietf-netconf-event-netconf
draft-ietf-netconf-event-restconf
draft-ietf-netconf-yang-push
Subscriptions for Event Notifications
NETCONF Transport
Pub/Sub Requirements
YANG Datastore Push
2015
2014
2016
IETF 93
IETF 91
IETF 92
IETF 94
IETF 95
OC-Telemetry
GitHub: openconfig-telemetry.yang
IETF 96
Restconf & HTTP Transport
IETF 97
RFC 7923
2017
IETF 98
draft-voit…
Notifications2
draft-openconfig-rtgwg…
gNMI

## Slide 20: Binding OpenC2 into the Network Configuration should be at the highest Aggregate Level Possible
It is more efficient (and safer) for OpenC2 to configure only a data field at the highest exposed level
That place changes
Location independent
Bounds of Protocol
Router / Switch
Example: Global ACL rules, QoS Class Definitions,
Example: VRF ACL, OSPF area
Example: User ACL rules, Authentication Keys
Hierarchy of Configuration Domains
Notes: Such mechanisms can be fortified with configuration checks to validate consistency across and within the Hierarchy

## Slide 21: Binding OpenC2 into the Network Info carried within the abstraction will vary
/
Applications
SP/WAN
Physical Infrastructure
(L1)
Resource Orchestration
(L3)
Virtualized
Infrastructure
(L2)
Network Services
Apps
Host/CPE
API
Compute & Storage
Agents
Client
Physical
Gateways/Switches/Routers
Virtual
Gateways/Routers
Storage
Virtual
Storage
Compute
Virtual Machines
Hypervisors
Scalable Cloud Platform
LAN/Campus
Overlay
Services
Physical
Switches
Physical
Switches
Virtual
Switches
Physical
Appliances
Virtual
Appliances
Overlays, VPNs, Slices, SLA Paths
Subscriber Mgmt
System Management
Workflow Management
Common Elementary Functions (Device Access, Data Store, Security,…)
SDN Controller
Orchestration
Network Management
Host/CPE
Acc/Agg
Access Aggr.
CPE
vCPE
Gateway
Edge
Core
vGW
PE
VR
Core
Optical/Transport
LAN/Campus
AP,
Access
Aggr.
Core
Leaf
Spine
Overlay
Leaf
NIC
vSwitch
GW
Services
Video
Distr.
FW
LB
vFW
vLB
PGW
SGW
vRR
Traffic Eng.
Custom Routing
Location Ctrl.
Mobility Mgmt.
Slicing
Service Mgmt.
Service X-connect
Network Orchestration
Infrastructure Provisioning
Topology
Positioning
Address Mapping
Distributed/Peering Protocols – □ BGP □ ISIS □ LISP □ VXLAN □ CAPWAP □ PMIP □ …
Security
Openstack
Virtual DataCenter

## Slide 22: Router Profile Mapping to OpenC2
  For a generic router profile, a context-independent language binding of OpenC2 won’t be generalized.
    Too many underlying technologies (e.g., VLAN, VRF, MPLS, EVPN, LISP, 802.11ah, VXLAN)
    Volume and churn of what is actually behind the router abstraction has spawned industries
  But we can provide a reference-mapping
    CLI: particular router, using a particular release, for selected network technologies
    YANG: subset of models, for selected network technologies
Actions on objects tightly controlled
Unstructured, non-standard, changes by release, designed for human scale
Comparing any two routers is non-trivial (e.g., 500+ page cheat sheet )
Actions and objects decoupled
Structured, early standards, changes by release, designed for machines
Comparing any two routers is easier, but the volume of information is huge (e.g., hundreds of models with up to hundreds of objects per software release )
This is why we have abstractions
(i.e., OpenC2)